## Slide 1
Constraints

## Slide 2
Budget: $400
Hardware Requirements:
  Must use PIC32 microcontrollers as the processors
  Must use provided Zumo motors
  Must use a robotic arm that costs less than $75
  Cannot use a line follower array
  Cannot use an overhead camera
Constraints

## Slide 3
38.1 cm by 38.1 cm Tic-Tac-Toe board with 12.7 cm by 12.7 cm squares
A rover with the robotic arm will move around the game board to draw tokens
The arm must draw the ‘X’s to be at least 4 cm long and ‘O’s to be at least 4 cm in diameter.
The ‘X’s and ‘O’s must be completely in the target square
The user will interact with a GUI to select moves
Project Requirements

## Slide 4
Robot Arm

## Slide 5
Decided on a 4-Servo ArmUno 2.0 - 3 axis motion + claw for the servo
Within the price constraints of the project,
and large enough to manipulate a dry erase
marker as needed
Choice of Robot Arm

## Slide 6
Each of the arm servos is controlled by a pulse width modulated signal with a 20ms period.
An arm control library provides an API tell the arm to perform complex and simple motions.
Simple motions are things like setting a servo angle. Complex motions are time dependant motion paths, defined as a series of arm positions and the speed to move between them.
Robot Arm Control

## Slide 7
To meet the project requirements, complex motions to draw “X” and “O” were created
The arm thread performs actions depending on a sent of enumerated command messages sent to it
After finishing each action, the arm thread sends and acknowledge message back to the navigation thread to indicate it is done.
Integration

## Slide 8
Motors

## Slide 9
Designed an API to:
Move rover forwards/backwards a given distance using encoders
Turn rover left/right a given angle using encoders
Asynchronously stop the motors
Incorporate a PID feedback control loop
Motor Control

## Slide 10
Implementation
Motor Thread:
Receives movement commands from navigation thread in it’s queue and controls the motors accordingly
Reads encoder values when timer messages are received every 100 ms in it’s queue and adjusts the motor PWM signals accordingly
Acknowledges sent to navigation queue when movements are complete

## Slide 11
Sensors

## Slide 12
Sensors are used to determine the rover’s location.
Sensor Type: Extra Long Force Sensitive Resistors
Functionality:
  Resistance is based on the amount of pressure applied
  Pressure decreases the resistance which in turn increases the Analog to Digital Converters readings
Force Sensitive Sensors
Notes: Based on project specifications we were unable to use the line follower array or overhead camera for rover navigation on our game board. To autonomously navigate the board used Force Sensitive Resistors to determine the rover’s location. 10 Sensors were placed in a grid format around the game board. Each sensor has two pins, one is connected to the PIC’s 5V input and the other to a pull down resistor which is connected to ground. The connection point between the pull down resistor and the Force Sensitive Sensor is then wired to one of the analog inputs on the PIC. The sensors resistance is based on the amount pressure applied to them, so when rover drive on top of the sensor, the resistance will decrease which in turn increases the Analog to Digital Converters reading. The Analog to Digital Converter was configured to support multiple analog input readings, using ADC scan mode.

## Slide 13
Implementation
Sensor Thread
Runs a calibration routine on start up.
Reads the value from the Analog to Digital Converter
Calls a conversion function:
  Compares the read value at each pin with a threshold value to determine whether the sensor has pressure.
Sends the converted value to the server
Notes: The Sensor Thread is ran on its own PIC. On startup the Analog to Digital Converter Interrupt will run a calibration routine that will take 2 readings of each Analog Pin. The two readings for each pin is then averaged together and the average value is then stored in a array The average value will sever as threshold comparison value that will be used in the conversion function.
This conversion function is also called in the interrupt. It takes the threshold value array as an input and return a 10 bit integer value as an output. Each bit in the integer value corresponds to a speciific sensor.
In the conversion function The value of each analog pin is compare to the threshold value and if the pin's value is greater then the threshold, this indicates that the sensor has pressure on it.
The corresponding bit in the 10 bit integer value, the corresponding bit is then converted to a 1. If there is no pressure, the corresponding bit value will remain a 0. This 10 bit value is then returned. The value is sent to the sensor queue.
In the main function of the program the value is then added to a json POST message which is sent to the server and stored in a database every half second.

## Slide 14
Communications

## Slide 15
Raspberry Pi was used as an access point
Base Http Server that uses multithreading to handle multiple requests
MongoDB to store Post request data
Sends a Json response to the client
Raspberry Pi HTTP Server

## Slide 16
Graphical User Interface

## Slide 17
Can select single player or two player mode
In single player, can select easy or hard difficulty for computer player
In easy mode, picks random open tile. In hard mode, uses priority algorithm to pick the best move.
Settings GUI

## Slide 18
Windows form GUI provides interface to enter human player moves and see computer player moves
Blocks entry of new moves until current move is done and shows when the game is over
Board on the left shows the current FSR state and the position of the rover on the board
Gameplay GUI

## Slide 19
Navigation

## Slide 20
After initialization the direction function is called, determining the shortest direction of travel.
The mapping state machine uses the current location as the state and changes states based on FSR input and Direction of travel.
  Each state handles error, the number of corrections is limited during a set time period.
Direction and Mapping

## Slide 21
Uses the direction, current position, FSR input, and the given move to send a series of commands to the motors and arm.
Command Function

## Slide 22
Reliability

## Slide 23
All server communication done using HTTP messages with JSON data bodies - the protocol designed in such a way that no single message between server and PIC is critical and will result in failure if it does not send/receive.
Internal queues and communication on PIC used same struct for all threads, proved to be very consistent without failure/deadlock risk.
Used the Python BaseHTTP server library - during testing of the gameplay, had intermittent issue where the server would lock up and require a restart - this was the most significant software related consistency issue.
Software Reliability

## Slide 24
More testing would be needed to get 100% reliability in board navigation.
Turning around corners ended up being the most difficult issue - high latency between the sensor PIC and rover PIC combined with uneven board (tape + wires) lead to a diminished turning accuracy for the rover.
Extensive testing of the arm draw “O” and draw “X” caused a degradation in the arm servos over time. Gradually lost ability to actuate to the necessary angles and would stall out - could be fixed with higher quality servos.
Hardware Reliability

## Slide 25
Robustness

## Slide 26
When the rover is angled wrong with a tread depressing its respective sensor it will attempt to correct a set number of times every 5 seconds.
If a tread depresses the wrong sensor the error correction will kick the rover completely off track. The rover will need to be reset on the sensor network.
When the server fails to send updated FSR data to the rover the rover will not know to transition its current location internally.
The rover always drifted slightly left. If the rover was straddling only the right FSR on a straight the rover would correct itself.
Handling under
extreme circumstances