## Slide 1
Rover Tic-Tac-Toe
Alex Nolan, Sajan Ronvelwala, Sasha Morgan, Thomas Bellerose
Fall, 2018

## Slide 2
A brief description of the section can be placed here. It does not need to be very long.
Overview

## Slide 3
Constraints

## Slide 4
Economic: $400 budget
Available Hardware: Couldn’t use line follower
Project Constraints

## Slide 5
Robot Arm

## Slide 6
Decided on a 4-Servo ArmUno 2.0 - 3 axis motion + claw for the servo
Within the price constraints of the project,
and large enough to manipulate a dry erase
marker as needed
Choice of Robot Arm

## Slide 7
Each of the arm servos is controlled by a pulse width modulated signal with a 20ms period.
An arm control library provides an API tell the arm to perform complex and simple motions.
Simple motions are things like setting a servo angle. Complex motions are time dependant motion paths, defined as a series of arm positions and the speed to move between them.
Robot Arm Control

## Slide 8
To meet the project requirements, complex motions to draw “X” and “O” were created
The arm thread performs actions depending on a sent of enumerated command messages sent to it
After finishing each action, the arm thread sends and acknowledge message back to the navigation thread to indicate it is done.
Integration

## Slide 9
Motors

## Slide 10
Designed an API to:
Move rover forwards/backwards a given distance using encoders
Turn rover left/right a given angle using encoders
Asynchronously stop the motors
Incorporate a PID feedback control loop
Motor Control

## Slide 11
Implementation
Motor Thread:
Receives movement commands from navigation thread in it’s queue and controls the motors accordingly
Reads encoder values when timer messages are received every 100 ms in it’s queue and adjusts the motor PWM signals accordingly
Acknowledges sent to navigation queue when movements are complete

## Slide 12
Sensors

## Slide 13
Sensors are used to determine the rover’s location.
Sensor Type: Extra Long Force Sensitive Resistors
Functionality:
  Resistive value is based on the amount of pressure applied
  Pressure decreases the resistance which in turn increases the Analog to Digital Converters readings
Force Sensitive Sensors

## Slide 14
Implementation
Sensor Thread
Calibration routine is instantiated during start

## Slide 15
Communications

## Slide 16
A brief description of the section can be placed here. It does not need to be very long.
Raspberry Pi HTTP Server

## Slide 17
Graphical User Interface

## Slide 18
A brief description of the section can be placed here. It does not need to be very long.
Settings GUI

## Slide 19
A brief description of the section can be placed here. It does not need to be very long.
Gameplay GUI

## Slide 20
Navigation

## Slide 21
The first zation is , determines the shortest direction of travel given a move.
Uses the current location as the state and changes states based on FSR input and Direction of travel.
Each state handles error, the number of corrections is limited during a set time period.
Direction and Mapping

## Slide 22
Uses the direction, current position, FSR input, and the given move to send a series of commands to the motors and arm.
Command Function

## Slide 23
Reliability

## Slide 24
A brief description of the section can be placed here. It does not need to be very long.
Robot Arm Control

## Slide 25
Robustness

## Slide 26
A brief description of the section can be placed here. It does not need to be very long.
Robot Arm Control